## Slide 1: Dual-Axis ECC: Vertical and Horizontal Error Correction for Storage and Transfer Errors
Giyong Jung, Hee Ju Na, Sang-Hyo Kim, and Jungrae Kim
Dept. of Electrical and Computer Engineering, Sungkyunkwan University, Republic of Korea
Notes: Hello, my name is giyong jung.
Today, I would like to talk about Our Strong error protection schemes, Dual-Axis ECC.

## Slide 2
Introduction
Prior Work
Dual-Axis ECC
Evaluation
Conclusion
Outline

## Slide 3: DRAM Evolution
Introduction
Chart: DRAM I/O Data Rate Trend
| 2000 | 2001 | 2002
DDR1 | 0.266 | 0.31 | 0.4
DDR2 | 0.533 | 0.66 | 0.7 | 0.8
DDR3 | 1.066 | 1.4 | 1.6
DDR4 | 2.133 | 2.8 | 3.2
DDR5 | 4.8 | 5.6 | 6.4
DRAM Evolution 2: Higher Data rate
DRAM Evolution 1: Higher Chip density
Chart: DRAM Density Trend
| 36526 | 38353 | 39083 | 39814 | 40544 | 41275 | 42005 | 42736 | 43466 | 44562 | 45658
Samsung | 0.0037 | 0.0073 | 0.015 | 0.028 | 0.07 | 0.1 | 0.13 | 0.17 | 0.18 | 0.23
SK Hynix | 0.0039 | 0.0071 | 0.012 | 0.023 | 0.06 | 0.08 | 0.11 | 0.16 | 0.19 | 0.22
Micron | 0.0035 | 0.0069 | 0.013 | 0.025 | 0.051 | 0.06 | 0.09 | 0.13 | 0.17 | 0.21
Notes: DRAM evolution has occurred in two aspects.
DRAM Vendors have continuely scaled down the manufacturing process to increase the chip density.
On another front, they also have approximately doubled its Input Output Transfer rate at each generations to serve huge bandwidth.

## Slide 4: Dark Side of DRAM Evolution
Introduction
Higher Chip density Storage Errors
Higher Data rate Transfer Errors
DIMM (x8 chips)
x8
Chip
x8
Chip
x8
Chip
DIMM (x8 chips)
x8
Chip
x8
Chip
x8
Chip
Notes: However, these evolutions cause different types of errors: storage and transfer errors.
Let’s talk about storage errors first.
A single DIMM mounts multiple DRAM chips to form a channel. For example, it mounts 8 x8 chips to achieve a 64-bit channel width.

## Slide 5: Dark Side of DRAM Evolution
Introduction
Higher Data rate Transfer Errors
DIMM (x8 chips)
x8
Chip
x8
Chip
x8
Chip
x8
Chip
DIMM (x8 chips)
Higher Chip density Storage Errors
[-Particle strike ]
[Wear Out ]
1
2
1: http://www.mrchsv.com/docs/Vanderbilt/Transient-SEE-Lecture.pdf
2: N. Mirabella, M. Ricci, I. Cal`a, R. Lanza, and M. Grosso,
“Testing singlevia related defects in digital VLSI designs,” Microelectronics Reliability.
Notes: In this moment, The increased chip density has made it even more vulnerable to issues like alpha particle strikes and DRAM wear out.

## Slide 6: Dark Side of DRAM Evolution
Introduction
Higher Data rate Transfer Errors
DIMM (x8 chips)
x8
Chip
x8
Chip
x8
Chip
x8
Chip
DIMM (x8 chips)
Higher Chip density Storage Errors
[-Particle strike ]
[Wear Out ]
1
2
1: http://www.mrchsv.com/docs/Vanderbilt/Transient-SEE-Lecture.pdf
2: N. Mirabella, M. Ricci, I. Cal`a, R. Lanza, and M. Grosso,
“Testing singlevia related defects in digital VLSI designs,” Microelectronics Reliability.
Channel Width (e.g., 64-bit)
64B Memory Transfer Block
Burst length (e.g., 8)
Notes: This issues result in serious problems.
A single DIMM transfers 64B of data in a read operation through multiple bursts to meet the cache line size.
This is called a memory transfer block.

## Slide 7: Dark Side of DRAM Evolution
Introduction
Higher Data rate Transfer Errors
DIMM (x8 chips)
x8
Chip
x8
Chip
x8
Chip
DIMM (x8 chips)
x8
Chip
64B Memory Transfer Block
DQ error
Chip error
Bit Flips
Higher Chip density Storage Errors
[-Particle strike ]
[Wear Out ]
1
2
1: http://www.mrchsv.com/docs/Vanderbilt/Transient-SEE-Lecture.pdf
2: N. Mirabella, M. Ricci, I. Cal`a, R. Lanza, and M. Grosso,
“Testing singlevia related defects in digital VLSI designs,” Microelectronics Reliability.
Notes: The fault within the chips results in bit flips in this 64B memory transfer block.
Some of them appear as relatively small granules, but sometimes it can cause entire chip failures, leading to widespread chip errors.

## Slide 8: Dark Side of DRAM Evolution
Introduction
Higher Data rate Transfer Errors
DIMM (x8 chips)
x8
Chip
x8
Chip
x8
Chip
DQS Signal
64B Memory Transfer Block
DIMM (x8 chips)
x8
Chip
64B Memory Transfer Block
DQ error
Chip error
Bit Flips
Higher Chip density Storage Errors
[-Particle strike ]
[Wear Out ]
1
2
1: http://www.mrchsv.com/docs/Vanderbilt/Transient-SEE-Lecture.pdf
2: N. Mirabella, M. Ricci, I. Cal`a, R. Lanza, and M. Grosso,
“Testing singlevia related defects in digital VLSI designs,” Microelectronics Reliability.
Notes: Now Let’s talk about transfer error.
Each chip in the DIMM has a DQ Strobe pin to provide data capture timing, and multiple DQ pins use this DQS signal to capture the data of each burst.

## Slide 9: Dark Side of DRAM Evolution
Introduction
Higher Data rate Transfer Errors
DIMM (x8 chips)
x8
Chip
x8
Chip
x8
Chip
DQS Error
64B Memory Transfer Block
DIMM (x8 chips)
x8
Chip
64B Memory Transfer Block
DQ error
Chip error
Bit Flips
Higher Chip density Storage Errors
[-Particle strike ]
1
2
[Wear Out ]
1: http://www.mrchsv.com/docs/Vanderbilt/Transient-SEE-Lecture.pdf
2: N. Mirabella, M. Ricci, I. Cal`a, R. Lanza, and M. Grosso,
“Testing singlevia related defects in digital VLSI designs,” Microelectronics Reliability.
Notes: However, errors can occur in the DQS signal.

## Slide 10: Dark Side of DRAM Evolution
Introduction
Higher Data rate Transfer Errors
DIMM (x8 chips)
x8
Chip
x8
Chip
x8
Chip
[Eye diagram ]
DQS Error
64B Memory Transfer Block
DIMM (x8 chips)
x8
Chip
64B Memory Transfer Block
DQ error
Chip error
Bit Flips
Higher Chip density Storage Errors
[-Particle strike ]
[Wear Out ]
1
2
1: http://www.mrchsv.com/docs/Vanderbilt/Transient-SEE-Lecture.pdf
2: N. Mirabella, M. Ricci, I. Cal`a, R. Lanza, and M. Grosso,
“Testing singlevia related defects in digital VLSI designs,” Microelectronics Reliability.
3: chrome-extension://efaidnbmnnnibpcajpcglclefindmkaj/https://ibis.org/summits
/feb18/muranyi2.pdf
3
Notes: Doubled I/O rate means the DQS toggle has also become twice as fast.
As a result, the timing margin is insufficient, significantly increasing the risk of DQS errors.

## Slide 11: Dark Side of DRAM Evolution
Introduction
Higher Data rate Transfer Errors
DIMM (x8 chips)
x8
Chip
64B Memory Transfer Block
DQ error
Chip error
Bit Flips
DIMM (x8 chips)
x8
Chip
x8
Chip
x8
Chip
Bit Flips
DQS Error
64B Memory Transfer Block
Higher Chip density Storage Errors
[-Particle strike ]
[Wear Out ]
1
2
1: http://www.mrchsv.com/docs/Vanderbilt/Transient-SEE-Lecture.pdf
2: N. Mirabella, M. Ricci, I. Cal`a, R. Lanza, and M. Grosso,
“Testing singlevia related defects in digital VLSI designs,” Microelectronics Reliability.
[Eye diagram ]
3: chrome-extension://efaidnbmnnnibpcajpcglclefindmkaj/https://ibis.org/summits
/feb18/muranyi2.pdf
3
Notes: This DQS error causes horizontal errors, bit flips, in all the bits that use this DQS signal.

## Slide 12
Introduction
Prior Work
Dual-Axis ECC
Evaluation
Conclusion
Outline
Notes: Now let’s look into prior works that have addressed these issues.

## Slide 13: Solutions of Errors
Prior Work
13
Storage Error Solutions : ECC
Transfer Error Solutions : CRC
ECC-DIMM (x4 chips)
Data
Chip
DIMM (x8 chips)
Data
Chip
Data
Chip
Data
Chip
Data
Chip
Data
Chip
Redun.
Chip
Redun.
Chip
Data
Chip
Data width (64-bit)
Redun. width (8-bit)
Notes: First, DIMM introduced Error Correcting Code as a solution for storage errors.
They mount additional redundancy chips on the DIMM to implement ECC.
In cases where you use the narrower data chips to compose a channel, such as X4 chips, you can apply a more robust ECC, called chipkill-correct.

## Slide 14: Solutions of Errors
Prior Work
14
Storage Error Solutions : ECC
Transfer Error Solutions : CRC
ECC-DIMM (x4 chips)
Data
Chip
DIMM (x8 chips)
Data
Chip
Data
Chip
Data
Chip
Data
Chip
Redun.
Chip
Redun.
Chip
Data
Chip
Data width (64-bit)
Redun. width (8-bit)
Notes: Let’s consider a scenario where one chip fails.

## Slide 15: Solutions of Errors
Prior Work
15
Storage Error Solutions : ECC
Transfer Error Solutions : CRC
ECC-DIMM (x4 chips)
Data
Chip
DIMM (x8 chips)
Data
Chip
Data
Chip
Data
Chip
Data
Chip
Redun.
Chip
Redun.
Chip
Chip Error (4-bit width)
Data
Chip
Notes: Then, during the process of transferring the memory block, the bits coming from this failed chip will contain errors.

## Slide 16: Solutions of Errors
Prior Work
16
Storage Error Solutions : ECC
  X4 DIMM provides Chipkill-Correct ECC
Transfer Error Solutions : CRC
ECC-DIMM (x4 chips)
Data
Chip
DIMM (x8 chips)
Data
Chip
Data
Chip
Data
Chip
Data
Chip
Redun.
Chip
Redun.
Chip
Chipkill-Correct
Data
Chip
Notes: However, since there is enough redundancy, you can correct these 4-bit wide chip errors.
This type of ECC, which can correct an entire chip failure, is called Chipkill-Correct ECC

## Slide 17: Solutions of Errors
Prior Work
17
Storage Error Solutions : ECC
Transfer Error Solutions : CRC
ECC-DIMM (x4 chips)
Data
Chip
DIMM (x8 chips)
Data
Chip
Data
Chip
Data
Chip
Data
Chip
Redun.
Chip
Redun.
Chip
Data
Chip
ECC-DIMM (x8 chips)
Redun.
Chip
Data
Chip
Notes: However, you cannot use this roubst chipkll-correct ECC when you use relatively wider chip to make a channel.

## Slide 18: Solutions of Errors
Prior Work
18
Storage Error Solutions : ECC
  A X8 Chip failure result in more wider errors
  Cannot provide chipkill-correct
Transfer Error Solutions : CRC
ECC-DIMM (x4 chips)
Data
Chip
DIMM (x8 chips)
Data
Chip
Data
Chip
Data
Chip
Data
Chip
Redun.
Chip
Redun.
Chip
Data
Chip
ECC-DIMM (x8 chips)
Redun.
Chip
Data
Chip
Chip Error (8-bit width)
Notes: When a wide-width chip fails, a wider 8-bit error will appear in the memory transfer block compared to the case of an X4 chip failure.
Due to insufficient redundancy to cover such a wide error, wider-chip based DIMM cannot provide chipkill-correct ECC

## Slide 19: Solutions of Errors
Prior Work
19
Storage Error Solutions : ECC
  DRAM Vendors adopt falut-bound concept
Transfer Error Solutions : CRC
ECC-DIMM (x4 chips)
Data
Chip
DIMM (x8 chips)
Data
Chip
Data
Chip
Data
Chip
Data
Chip
Redun.
Chip
Redun.
Chip
Data
Chip
ECC-DIMM (x8 chips)
Redun.
Chip
Data
Chip
OR
Confine errors within L or R nibble
Notes: To overcome this, DRAM vendors introduced the concept of a fault bound since DDR5.
The intent of this concept is to carefully organize the internal components of the DRAM, such as the mapping between rows and data pins, so that errors caused by chip failures are confined to only the left or right nibble.
It allows 4-bit wide error within a memory transfer block.

## Slide 20: Solutions of Errors
Prior Work
20
Storage Error Solutions : ECC
  Provide Half-Chip Correct (HCC) to X8 DIMM
Transfer Error Solutions : CRC
ECC-DIMM (x4 chips)
Data
Chip
DIMM (x8 chips)
Data
Chip
Data
Chip
Data
Chip
Data
Chip
Redun.
Chip
Redun.
Chip
Data
Chip
ECC-DIMM (x8 chips)
Redun.
Chip
Data
Chip
OR
Half-Chip Correct
Notes: Then, these errors are becoming narrow errors, similar to those from an X4 chip, and can all be corrected. This is called Half-Chipkill Correct.

## Slide 21: Solutions of Errors
Prior Work
21
Storage Error Solutions : ECC
  Provide Half-Chip Correct (HCC) to X8 DIMM
Transfer Error Solutions : CRC
  Transfer checksums using additional beats
ECC-DIMM (x4 chips)
Data
Chip
DIMM (x8 chips)
Data
Chip
Data
Chip
Data
Chip
Data
Chip
Redun.
Chip
Redun.
Chip
Data
Chip
ECC-DIMM (x8 chips)
Redun.
Chip
Data
Chip
Additonal Beats
Longer Burst
64B Memory Transfer Block
OR
Half-Chip Correct
Notes: On another front, DIMM introduced Cyclic Redundancy Check (CRC) as a solution for Transfer errors since DDR4.
It transmits checksums along with the memory transfer block through additional beats, which requires longer bursts for each data transmission.

## Slide 22: Solutions of Errors
Prior Work
22
Storage Error Solutions : ECC
  Provide Half-Chip Correct (HCC) to X8 DIMM
Transfer Error Solutions : CRC
  DQS error results in wider error in X8 DIMM
  ECC cannot deal with this wider errors
ECC-DIMM (x4 chips)
Data
Chip
DIMM (x8 chips)
Data
Chip
Data
Chip
Data
Chip
Data
Chip
Redun.
Chip
Redun.
Chip
Data
Chip
ECC-DIMM (x8 chips)
Redun.
Chip
Data
Chip
Additonal Beats
Longer Burst
64B Memory Transfer Block
DQS Error
OR
Half-Chip Correct
Notes: In this situation, Let’s say a DQS error occurs.
A single DQS error results in wide multiple bit flips associated with it.
As I mentioned earlier, insufficient redundancy in ECC cannot handle such wide error.

## Slide 23: Solutions of Errors
Prior Work
23
Storage Error Solutions : ECC
  Provide Half-Chip Correct (HCC) to X8 DIMM
Transfer Error Solutions : CRC
  CRC provides DQS Error detection
ECC-DIMM (x4 chips)
Data
Chip
DIMM (x8 chips)
Data
Chip
Data
Chip
Data
Chip
Data
Chip
Redun.
Chip
Redun.
Chip
Data
Chip
ECC-DIMM (x8 chips)
Redun.
Chip
Data
Chip
Additonal Beats
Longer Burst
64B Memory Transfer Block
DQS Error detection
OR
Half-Chip Correct
Notes: That’s why CRC was introduced, allowing the receiver to use the received checksum to detect DQS errors.

## Slide 24: Solutions of Errors
Prior Work
24
Storage Error Solutions : ECC
  Cost : additional chip(s)
Transfer Error Solutions : CRC
  Cost : additional beat(s)
ECC-DIMM (x4 chips)
Data
Chip
DIMM (x8 chips)
Data
Chip
Data
Chip
Data
Chip
Data
Chip
Redun.
Chip
Redun.
Chip
Data
Chip
ECC-DIMM (x8 chips)
Redun.
Chip
Data
Chip
Additonal Beats
Longer Burst
64B Memory Transfer Block
DQS Error detection
OR
Half-Chip Correct
Notes: So, in conclusion, we are paying two different costs to address different types of errors.
ECC requires additional chips to store redundancy, while CRC demands additional beats to transmit checksums.
Of course, one might ask why we don't just increase the redundancy chips and solve everything with ECC, but that approach would be highly inefficient.

## Slide 25: Solutions of Errors
Half-Chip Correct
Prior Work
25
Storage Error Solutions : ECC
  Cost : additional chip(s)
Transfer Error Solutions : CRC
  Cost : additional beat(s)
ECC-DIMM (x4 chips)
Data
Chip
DIMM (x8 chips)
Data
Chip
Data
Chip
Data
Chip
Data
Chip
Redun.
Chip
Redun.
Chip
Data
Chip
ECC-DIMM (x8 chips)
Redun.
Chip
Data
Chip
Additonal Beats
Longer Burst
64B Memory Transfer Block
DQS Error detection
OR
We need integrated, efficient solution for both types of errors
Notes: Rather, we need integrated, efficient solution for both types of errors.

## Slide 26
Introduction
Prior Work
Dual-Axis ECC
Evaluation
Conclusion
Outline

## Slide 27: Overview
Dual-Axis ECC
Dual-Axis ECC (DA-ECC) should correct
  Half-chip error
  2 independent DQ errors
  1 DQS error
DDR5 ECC-DIMM (x8 chips)
Redun.
Chip
Data
Chip
Correctable 1 :
Half-chipkill
Correctable 2 :
2 DQ errors
Correctable 3 :
DQS error
Sub-channel0
Sub-channel1
Notes: The main goal of DA-ECC is to provide correction capability for Half-chip, 2 independent DQ errors, and 1 DQS error with a single Redundancy chip.

## Slide 28: Symbol Layout
Dual-Axis ECC
Dual-Axis ECC (DA-ECC) symbol layout
  2 codewords from 1 Memory Transfer Block.
  8-bit vertical symbol-based Reed-Solomon Code (RS-Code).
  8 redundant symbols provide upto 4 symbol correction (HCC and 2-DQs).
Data
Chip
Data
Chip
Redun.
Chip
Data
Chip
Data
Chip
Vertical Symbol (8-bit)
Codeword 0
Codeword 1
DDR5 Burst Length(16)
(32 + 8 pins)
Correction
Notes: Our DA-ECC targets X8 DDR5.
A subchannel in X8 DDR5 consists of 4 data chips and 1 redundancy chip.
Since there are 4 chips with 8 pins each, the subchannel data width is 32 bits, and to match the 64B cache line size, the burst length is doubled to 16.
We divide one memory transfer block into two codewords.
Within a codeword, we group 8 bits vertically to form a vertical symbol.
In other words, one codeword consists of 32 data symbols and 8 redundancy symbols.
We then apply Reed-Solomon (RS) Code to this symbol-based codeword.
I won’t go into the theoretical details of RS code.
But the result is that the 8 redundancy symbols within a codeword provide correction capability for up to 4 symbols, half of the number of redundancy symbols, which achieves Half-Chipkill and 2 independent DQ error .
Now, the challenge is that we also need to provide DQS error correction capability.

## Slide 29: Leveraging Under-Utilized Redundancy
Dual-Axis ECC
Under-utilized redundancy in DDR5 ECC DIMM
  8-bit symbol provides 255-symbol codeword.
  40-pin interface uses only 40 out of 255 symbols, leaving 99.99999977% unused.
Data
Chip
Data
Chip
Redun.
Chip
Data
Chip
Data
Chip
Vertical Symbol (8-bit)
Codeword
Shortened Codeword (40-Symbol)
Shortened area
(215 “0” Symbols)
Original Codeword (255-Symbol)
Notes: To achieve this, we will use the under-utilized redundancy.
In fact, the 25% redundancy rate, is not enough to cover an entire chip failure but when used only for Half-Chip correction, there is a lot of wasted redundancy.
The 8-bit symbol allows a codeword to be composed of 255 symbols.
However, the 40-pin configuration of DDR5 uses only 40 of these symbols, so the remaining 215 symbols are simply treated as zeros during the encoding and decoding process.
Only 2.3 multipled by 10 to -7 percent of the redundancy is used for half-chipkill correct, leaving a huge amount of redundancy unused.
Our goal is to exploit under-utilized redundancy for DQS error correction.

## Slide 30: Finding H-matrix
Dual-Axis ECC
Codeword
H-matrix
ECC utilizes Syndrome based decoding
  Parity-check matrix “H” determines the mapping between errors and syndromes.
  Each syndrome indicates the position & value of error.
  All syndromes of target errors should be unique.
Syndrome
Syndrome
Decoding
Codeword
Notes: To leverage the under-utilized redundancy, We need to find an elegant parity check matrix, “H”.
During the decoding process, the memory controller gets codeword from DIMM and multiples it with the H-matrix to obtain the syndrome.
Then, it puts this syndrome into the decoding logic, the position and value of the error can be determined, allowing for correction.
So, it necessitate a one-to-one mapping between all of the target errors and syndromes to achieve correction capability.
I will not explain the mathematical properties that the H-matrix should have or the procedure for finding the H-matrix. You can check my paper for details.

## Slide 31: Finding H-matrix
Dual-Axis ECC
Founded H-matrix
  DA-ECC H matrix with primitive polynomial = 0x15F.
  Only exponents of s are shown.
Notes: This is the H-matrix we have found.
It generates unique syndromes for HCC and upto two adjacent horizontal errors, allowing the correction for Half chip and independent 2 DQ and single DQS error correction.

## Slide 32: Decoder
Dual-Axis ECC
Decoder
Codeword
(320b)
Syndrome
generator
Codeword
Detector
Syndrome
Data
Data
(256b)
DQS - LUT
Codeword
HCC
corrector
Decision
HCC result
LUT result
Detection result
Result
(2b)
Decision
result
Corrected
data
Corrected
data
Notes: This figure present the decoding process of DA-ECC.
The gray section indicate that decoder detect the error and forward the non-error data immediately to minimize latency.
The blue components represent the newly added components in DA-ECC, which include a lookup table containing information for additional DQS error correction.

## Slide 33
Introduction
Motivation
Dual-Axis ECC
Evaluation
Conclusion
Outline
Notes: Next is evaluation and conclusion

## Slide 34: Reliablity
Reliability Against Storage Errors Result
Evaluation
Error Scenario | Decoding Result | CRC+ SEC_DED | CRC+ 4bit SSC | CRC+ 8bit HCC | CRC+ QPC | DA-ECC
1 bit | SDC (%) | 0 |  |  |  | 
2 bit | SDC (%) | 0 | 3.77 | 0.88 | 0 | 0
1 chip | SDC (%) | 0 | 0.16 | 0 | 1E-8 | 3E-8
Half-chip | SDC (%) | 0 | 0 | 0 | 0 | 0
2 chips | SDC (%) | 0 | 0.16 | 0 | 1E-8 | 1E-8
[ Reliablity against storage errors]
DA-ECC provides same or even better undetected rate (SDC) against Storage errors than other (SOTA ECC+CRC)
Notes: This table shows the reliability against storage errors for various SOTA ECC plus CRC and our DA-ECC.
SDC refers to the undetected rate, meaning the proportion of errors that go unnoticed.
We can see that DA-ECC achieves similar or even better reliability compared to the others, without relying on CRC.

## Slide 35: Reliablity
Reliability Against Transfer Errors Result
Evaluation
Error Scenario | Decoding Result | CRC+ SEC_DED | CRC+ 4bit SSC | CRC+ 8bit HCC | CRC+ QPC | DA-ECC
1 DQ | SDC (%) | 0 |  |  |  | 
Consecutive 2 DQs | SDC (%) | 0 | 0.00015 | 0 | 0 | 0
Random 2 DQs | SDC (%) | 0 | 0.00089 | 0 | 0 | 0
1 DQS | SDC (%) | 0 |  |  |  | 
Consecutive 2 DQS | SDC (%) | 0 |  |  |  | 
[ Reliablity against transfer errors]
DA-ECC provides same or even better undetected rate (SDC) against Transfer errors than other (SOTA ECC+CRC)
Notes: This table also shows that for transfer errors, DA-ECC demonstrates similar or even better reliability compared to CRC plus ECC approaches, without relying on CRC.

## Slide 36: IPC & Energy
IPC Speed-up & DRAM Energy Consumption Reduction
  Can speed up SPEC benchmarks by upto 1.2%
  Can reduce DRAM energy consumption by upto 8.2%
Evaluation
Chart: Noramlized DRAM Energy
| mix1 | mix2 | mix3 | mix4 | mix5 | mix6 | mix7 | mix8 | mix9 | mix10 | mix11 | intensive | non_intensive | total
(NoCRC)/RCRC | 0.94517 | 0.95677 | 0.97632 | 0.96793 | 0.99541 | 0.9948 | 0.95797 | 0.96791 | 0.96434 | 0.9935 | 0.99205 | 0.95329 | 0.99394 | 0.97369
(NoCRC)/RWCRC | 0.91814 | 0.92076 | 0.96052 | 0.94548 | 0.99165 | 0.9899 | 0.9182 | 0.9492 | 0.94062 | 0.98846 | 0.98572 | 0.91903 | 0.98893 | 0.95491
Chart: Normalized IPC
| mix1 | mix2 | mix3 | mix4 | mix5 | mix6 | mix7 | mix8 | mix9 | mix10 | mix11 | mem_intensive | non_intensive | total
DA-ECC / RCRC | 1.0037 | 1.0065 | 1.0074 | 1.0122 | 1.0005 | 0.99983 | 1.0052 | 1.0074 | 1.0023 | 1.0007 | 1.0008 | 1.0057 | 1.0004 | 1.0042
DA-ECC / RWCRC | 1.0135 | 1.0129 | 1.0103 | 1.0163 | 1.0007 | 1.0002 | 1.0162 | 1.012 | 1.0065 | 1.0002 | 1.0017 | 1.0137 | 1.0007 | 1.0082
Notes: In this way, DA-ECC can eliminate CRC and remove the IPC and energy consumption overheads caused by the additional beats required for CRC.
It achieved up to a 1.2% IPC speedup and an 8.2% reduction in energy consumption.

## Slide 37: Decoder
Decoder Overhead
  Overheads of additional components are negligible.
Evaluation
Area () | 24,000
Power () | 12.43
Latency () | 0.33
 | 24,000
 | 12.43
 | 0.33
Notes: This table shows the decoder overhead.
The area overhead is not significant, and considering that correction part operates only when errors are detected, power and latency overheads are negligible.

## Slide 38: Conclusion
Dual-Axis ECC
  Unified, efficient method against both types of errors
Benefit
  Maintain reliability without CRC
  1.2% speed-up & 8.2% energy consumption reduction by removing CRC
Cost
  Negligible Decoder overheads
Conclusion
Ⅴ